ART. 6437

ELECTRIC BATTERY FIELD LINE STRIPER SPECIFICATIONS

Electric battery field line striper to spray water based non-toxic liquid turf paint.

The field line striper is composed of: tubular steel frame finished with blue-tinted white polyester powder, lead-free and in full compliance with current environmental regulations, with three 260 mm diameter pneumatic wheels, diaphragm pump assembly, two speeds, maximum pressure 2.7 bar, maximum capacity 1.9 l/min, rechargeable 12 V DC/2.5 A battery (12 hour cycle for a full charge, charge autonomy about 4-5 football fields), battery charger supplied (input voltage 230V/50 HZ, output voltage 12 V DC/500 mA). Noise: LWA less than 70 db EN ISO 3744/ (hearing protection not required for the operator), 18 l capacity polyethylene paint tank, spray unit with adjustable height brass nozzle, lateral striper unit adjustable from 0 cm to 20 cm, made of galvanized steel.

Total weight of the assembly (empty): 20 Kg.